## Slide 1
8-BIT SIGNED BINARY REPRESENTATION
Combinational vs Sequential • Clock • Latches • Flip-Flops • Registers • Counters • FSM
DIGITAL LOGIC & SEQUENTIAL CIRCUITS

## Slide 2
1. 8-Bit Signed Binary Representation
Understanding the data stored inside a digital system
An 8-bit word contains eight binary digits: b7 b6 b5 b4 b3 b2 b1 b0.
In 2’s-complement representation, the most significant bit (MSB) indicates the sign.
8-bit signed range: −128 to +127.
Positive values are represented directly; negative values are obtained by inverting the bits and adding 1.
Example: +13 = 00001101 → invert = 11110010 → +1 = 11110011 = −13.
Registers, counters and other sequential circuits can store these 8-bit signed values from one clock cycle to the next.
8-bit signed range: −128 to +127
2

## Slide 3
2. Combinational vs Sequential Circuits
The key difference is memory and dependence on previous states
COMBINATIONAL Output depends only on current inputs. Examples: adders, MUX, decoders, comparators
SEQUENTIAL Output depends on current inputs + previous state. Uses memory elements, clock, latches or flip-flops.
An 8-bit adder is combinational: its output changes when the inputs change.
An 8-bit register is sequential: it remembers the stored binary value until it is updated.
Sequential circuits are therefore essential when a digital system must remember data or follow a sequence of operations.
3

## Slide 4
3. Clock & Latches
Controlling when stored information changes
CLOCK Periodic timing signal ↑ ↑ ↑ ↑ | | | | Controls state changes
LATCH Level-sensitive Can respond while its enable/control level is active.
CLOCK EDGE Rising edge: ↑ Falling edge: ↓ Flip-flops usually respond to one edge.
The clock provides a common timing reference for sequential circuits.
A latch is level-sensitive, while an edge-triggered flip-flop changes state at a clock edge.
Clocked storage lets an 8-bit value be captured and held predictably.
4

## Slide 5
4. Flip-Flops & D Flip-Flop
A flip-flop stores one bit of information
FLIP-FLOP 1 bit of storage Q = stored state Q̅ = complement
D FLIP-FLOP D = data input CLK = clock Q(next) = D at the active clock edge
8-BIT STORAGE 8 D flip-flops = 8-bit register Example: 11110011
A D flip-flop removes the ambiguity of what data should be stored: the value at D is transferred to Q on the active clock edge.
Eight D flip-flops can store one complete 8-bit signed binary number.
Example: 11110011 can remain stored as −13 until a new value is clocked in.
5

## Slide 6
5. Registers
Groups of flip-flops used to store multi-bit data
D7 D6 D5 D4 D3 D2 D1 D0
8 D FLIP-FLOPS
Q7 Q6 Q5 Q4 Q3 Q2 Q1 Q0
8-BIT REGISTER Stores one 8-bit value
An n-bit register requires n storage elements such as D flip-flops.
An 8-bit register can hold signed values from −128 to +127 when interpreted using 2’s complement.
Registers are used for temporary data, operands, results and control information.
6

## Slide 7
6. Shift Registers: SISO & SIPO
Moving binary data one bit at a time
SISO Serial In → [FF] → [FF] → [FF] → [FF] → Serial Out Data enters and leaves one bit at a time.
SIPO Serial In → [FF] → [FF] → [FF] → [FF] ↓ Parallel Outputs Serial data becomes a multi-bit word.
SISO = Serial-In Serial-Out: useful for delaying or transmitting data serially.
SIPO = Serial-In Parallel-Out: useful for converting a serial bit stream into a parallel binary value.
With 8 stages, an 8-bit signed binary word can be shifted through the register over successive clock pulses.
7

## Slide 8
7. Counters
Sequential circuits that change state according to clock pulses
CLOCK ↓ COUNTER ↓ 0000 → 0001 → 0010 → 0011 → …
8-BIT COUNTER 00000000 00000001 00000010 ... 11111111 → repeats
SIGNED INTERPRETATION The same bit pattern can be interpreted as 2’s-complement signed data when required.
Counters advance through a predefined sequence of states.
An 8-bit binary counter has 256 distinct states before returning to its starting state.
Important: an ordinary binary counter counts bit patterns; interpreting those patterns as signed numbers is a separate operation.
8

## Slide 9
8. Program Counter (PC)
A special register that keeps track of the next instruction
PROGRAM COUNTER PC = address of next instruction Clock → PC updates → Instruction Memory reads address
CPU FLOW PC → Instruction Fetch ↓ Decode → Execute ↓ PC update
The program counter is a sequential storage element, normally implemented as a register.
On each instruction cycle, the PC can be updated to the next sequential address or changed by a branch/jump.
The clock coordinates these updates so the processor executes instructions in the intended sequence.
9

## Slide 10
9. Finite State Machine (FSM)
Representing a system as a set of states and transitions
STATE A IDLE
STATE B READ
STATE C EXECUTE
Clocked state register
An FSM consists of a finite number of states, transitions and outputs.
The current state is stored using flip-flops; the clock controls when the FSM changes state.
Example processor sequence: FETCH → DECODE → EXECUTE → FETCH.
FSMs are widely used in controllers, communication systems and digital processors.
10

## Slide 11
THANK YOU
8-Bit Signed Binary Representation