## Slide 1
8-BIT SIGNED BINARY REPRESENTATION
K-Maps • Adders • Subtraction • MUX • Comparators • Code Converters • ALU
DIGITAL LOGIC & COMBINATIONAL CIRCUITS

## Slide 2
1. 8-Bit Signed Binary Representation
How positive and negative integers are stored using 8 bits
An 8-bit binary number contains 8 positions: b7 b6 b5 b4 b3 b2 b1 b0.
In 2’s-complement representation, the MSB acts as the sign indicator: 0 → non-negative, 1 → negative.
8-bit signed range: −128 to +127.
Positive numbers are written normally; to represent a negative number, invert all bits and add 1.
Example: +13 = 00001101 → invert = 11110010 → +1 = 11110011 = −13.
2’s complement is especially useful because the same binary adder hardware can perform both addition and subtraction.
−128 ← 8-bit signed values → +127
2

## Slide 3
2. K-Maps
Simplifying Boolean logic before implementing a circuit
Karnaugh Maps provide a visual method for minimizing Boolean expressions.
Adjacent 1s are grouped for SOP simplification; adjacent 0s are grouped for POS simplification.
Groups are made in powers of two: 1, 2, 4, 8, … cells.
In signed arithmetic systems, K-Maps can simplify control and detection logic, such as sign or overflow conditions.
Fewer terms and fewer gates generally produce a simpler combinational circuit.
A\B
0
1
0
1
0
1
1
1
Group adjacent 1s → simplified expression
3

## Slide 4
3. Combinational Circuits
The output depends only on the present input values
Combinational circuits do not store previous states.
Common examples: adders, subtractors, decoders, encoders, multiplexers, comparators and code converters.
These circuits are built from logic gates such as AND, OR, NOT, XOR and NAND.
For an 8-bit system, individual 1-bit circuits can be connected in parallel or cascaded to process 8-bit data.
Together, these blocks form the datapath of larger digital systems such as an ALU.
INPUTS → LOGIC CIRCUIT → OUTPUTS
4

## Slide 5
4. Half Adder & Full Adder
Basic building blocks for binary addition
HALF ADDER Inputs: A, B Sum = A ⊕ B Carry = A · B
FULL ADDER Inputs: A, B, Cin Sum = A ⊕ B ⊕ Cin Cout = AB + Cin(A ⊕ B)
8-BIT ADDER 8 full adders connected together Cout → next Cin
Half adder adds two bits but has no carry-in.
Full adder adds A, B and an incoming carry.
Eight full adders can be cascaded to perform 8-bit binary addition.
5

## Slide 6
5. Binary Subtraction & Adder/Subtractor
Using 2’s complement to perform subtraction
Binary subtraction can be converted into addition using 2’s complement.
To calculate A − B: take the 2’s complement of B and add it to A.
Example: 7 − 3 → 00000111 + (2’s complement of 00000011 = 11111101) = 00000100.
An adder/subtractor combines both operations using XOR gates and a control signal.
When SUB = 0, B passes unchanged → addition. When SUB = 1, B is complemented and 1 is added → subtraction.
A ─────────────┐ ADDER ─→ RESULT B ─→ XOR ────────┘ ↑ SUB
SUB = 0 → A + B SUB = 1 → A − B
6

## Slide 7
6. Decoder & Encoder
Converting between coded inputs and one-hot outputs
DECODER n inputs → 2ⁿ outputs Example: 2 → 4 decoder Only one output is active for a valid input.
ENCODER 2ⁿ inputs → n outputs Example: 4 → 2 encoder Converts an active input into a binary code.
Decoders are useful for selecting one operation, memory location or control line.
Encoders perform the reverse type of conversion.
In an ALU or digital controller, these blocks can translate operation codes into control signals.
7

## Slide 8
7. Multiplexer & Comparator
Selecting data and comparing signed values
MUX Many inputs → one output Select lines decide which input reaches the output. 4:1 MUX → 2 select lines
COMPARATOR Checks A and B and produces A > B, A = B, or A < B. For signed values, the sign bit must be interpreted correctly.
A multiplexer can select between arithmetic and logic results inside an ALU.
Comparators can be designed for equality, magnitude or signed/unsigned comparison.
Example: in signed 8-bit numbers, 11111111 represents −1, not +255.
8

## Slide 9
8. Code Converters
Changing one binary coding scheme into another
Code converters are combinational circuits that translate information from one code to another.
Examples: Binary ↔ Gray, Binary ↔ BCD and BCD ↔ Excess-3.
Conversion is usually designed using truth tables, Boolean expressions and K-Maps.
Example: Gray code is useful in applications where reducing transition errors is important.
For an 8-bit digital system, code converters can be placed between input devices, processing logic and output/display circuits.
BINARY 1011
→
GRAY 1110
Truth Table → K-Map → Logic Gates
9

## Slide 10
9. ALU — Arithmetic Logic Unit
The ALU brings the major combinational building blocks together
A (8-bit)
B (8-bit)
ARITHMETIC ADD / SUBTRACT
LOGIC AND / OR / XOR
MUX SELECT OPERATION
RESULT 8-bit
COMPARE / FLAGS Zero • Carry • Sign • Overflow
An ALU receives binary operands and a control signal indicating the required operation.
Adders and subtractors handle arithmetic; logic gates handle bitwise operations; MUXes select the final result.
Signed 8-bit operations use 2’s complement and must account for overflow when interpreting results.
10

## Slide 11
THANK YOU
8-Bit Signed Binary Representation